## Slide 1: COURSE TITLE: OIL SEEDS PROCESSING AND UTILISATION
COURSE CODE: FST 504
By
Dr. Dupe Temilade Otolowo,
Department of Food Science and Technology, Mountain Top University,
Nigeria

## Slide 2
DISCRIPTION OF OIL SEEDS AND NUTS
Oilseeds and nuts are oil-bearing grain or fruit-like food crops. They are rich sources of vegetable fats and oils in addition to other nutritive values such as; provision of calories and vitamins.
Some grows wild (e. g. oil palm) while others are cultivated (e.g. groundnut, soybean); oil palm is also cultivated
They are generally low in moisture content. But must be fully dried before storage to avoid quality deterioration.
INTRODUCTION
Examples includes; groundnut, oil palm fruit, palm kernel, soybean, melon seeds, coconut fruit, corn, cotton, sunflower, rapeseed/canola, linseed/flax-seed, etc.
LECTURE 1

## Slide 3
Processing of Selected Oil Seeds, Nuts and Fruits
The processing of oil seeds and nuts is done generally to extract the oil in them. Traditional, small-scale and industrial levels of operations are available.
The traditional method of oil extraction is characterised by manual operations which yields crude, unrefined oil while the small-scale and industrial scale employed various mechanical oil extractors with devices inbuilt or detached mechanism for refining.
The technology generally involve the crushing of the oil seeds, nuts or fruits under certain conditions followed by the pressing of the resulted mass or cake to obtain the oil.

## Slide 4
Coconut fruit
Cracking shell
Crushing the meat
Mixing with water (at 100oC)
Pressing/filtering meat cake
Boiling water (vapour)
Refining /modification impurities
Refined Coconut oil
Oil Press from Coconut

## Slide 5
Home Scale Production of Groundnut Oil
Sorting
Cleaning
Sun drying for 8 days
Roasting at 150-200oC/20-30 min
Peeling/winnowing
Grinding
Mixing with water (1:4) /boiling/8-10 h
Separate paste
Groundnut seeds
Oil slurry
Boiling/1-4 h
Cooling at room temp
Packaging / Storage
Excess moisture

## Slide 6
Production of palm oil from palm fruit
Fruit fermentation Loosen fruit base from spikelets
Palm fruits bunch
Bunch chopping Facilitate manual removal of fruit
Fruit sorting Remove fruit from spikelets
Fruit boiling Sterilize and stop enzymatic spoilage, coagulate protein and expose microscopic oil cells
Fruit digestion Rupture oil-bearing cells to allow oil flow during extraction while separating fibre from nuts
Mash pressing Release fluid palm oil from ruptured oil cells using applied pressure
Oil purification Boil mixture of oil and water to remove water-soluble gums and resins, dry decanted oil by further heating
Fibre-nut separation Separate de-oiled fibre from palm nuts
Second Pressing Recover residual oil for use as soap stock

## Slide 7
Soybean
Cleaning
Drying
Dehulling by conventional, hot, or Esher wyss dehulling system
Conditioning/tempering
Flaking
Oil extraction Meal
Crude soya oil
Meal desolventizing
Production of Oil from Soybean
reduce mc (10%) and prevent moldiness
to pre-heating/cook the seeds improves flaking/extraction
Desolventizing

## Slide 8
Importance of Oilseed Drying before Processing/Storage
Reduces the moisture content of oilseeds to minimise degradation in storage.
Drying prevents moldiness of seeds and Aflatoxins (poisons produced by Aspergillus flavus) contamination either in the oil or the oil cake.
For example, soybeans are often received at 13% mc and need to be dried to 10% mc to facilitate efficient hull removal.
Improve the effectiveness of downstream processing. Large, vertical, open-flame grain dryers with multiple columns can be used for oilseeds drying. The upper portion of the columns is used for drying and lower section is for cooling.

## Slide 9
Shea Butter Processing
Washing
Sun drying
Boiling/1-3 h
Dehusk
Cracking into small pieces
Roasting at 85-100oC/2-3 h
Separate meal
Shea nuts
Fat slurry
Boiling
Cooling
Storage
Mill/Pressing
Remove the remaining moisture
Remove greater part of moisture

## Slide 10
OIL EXTRACTION FROM OILSEEDS
Methods of Oil Extraction from Oilseeds
There are only a few basic extraction methods to obtain fats and oils from animal, marine and vegetable sources which is followed by various refining and modification procedures. These include:
rendering,
pressure expelling and
solvent extraction.
LECTURE 2

## Slide 11
Rendering
Meat scraps are heated in steam or water to cause the fat to melt. The melted fat then rises and water and remaining tissue settle below.
The melted fat is then separated by skimming or centrifugation.
Rendering could be done by:
-dry heat under vacuum to remove moisture,
-wet rendering utilizes water steam, and
-low temperature rendering with enough heat to melt the fat- produce fat of lighter colour and less meaty flavour.
Rendering is also used to obtain oil from fish tissues.

## Slide 12
Pressing or Expelling/Filtering
This squeeze oil from oilseeds by mechanical presses and expellers or manual pressing of pre-ground oilseed. Prior to manual pressing, some preheating and addition of water can improve oil yield.
The heat from cooking or grinding should not be excessive to prevent darkening of oil colour. Expelled oil is pumped through multiple filter or by centrifugal clarification to removed seed residues. With some seeds e.g. Corn, only the germ of the seed is pressed to yield oil.

## Slide 13
Solvent Extraction
Employed in large-scale oil production.
Non-toxic fat solvent such as hexane is used to remove oil from cracked or ground seeds at low temperature.
Yield more oil than by pressing.
Combined processes employ pressing to remove most of the oil followed by solvent extraction to remove final traces.
The spent meal must be desolventised.

## Slide 14
Choice of solvents
An ideal solvent for the oil extraction should possess the following properties:
Good solubility of the oil.
Poor solubility of non-oil components.
High volatility (i.e. low boiling point), for feasibility and easy removal of the solvent from the micella and the meal by evaporation.
Yet, the boiling point should not be too low
Low viscosity
Low latent heat of evaporation, so that less energy is needed for solvent recovery.
Low specific heat, so that less energy is needed for keeping the solvent and the micella warm.
The solvent should be chemically inert to oil.
Absolute absence of toxicity and carcinogenicity.
Non-inflammable and non-explosive.

## Slide 15
Oil Refining
Degumming by hydration- to remove fat-like substance (such as phospholipids (phosphatides) fat-protein complexes). Water degumming process cannot achieve total removal of the gum, therefore the oil stream is further treated with alkali.
Neutralization or Caustic refining- to remove free fatty acids, phosphatides other unwanted materials using caustic soda. Some processors retreat crude oil with phosphoric acid to hydrate the phosphatides that are not water hydratable.
Bleaching over charcoal or various adsorbent clays and earths - to remove plant pigments, residual soap, metals, and phosphatides (gum) content
Deodorization- to remove odorous compounds by heat and vacuum or sometimes by adsorption onto activated charcoal
Winterization- to remove sufficient saturated triglycerides or wax so as to have a product higher in unsaturated fatty acid.
LECTURE 3

## Slide 16
Anti-nutritional factors in oil seeds
Fibre: High fibre content of most oilseed meals limit the availability of nutrients in the meal and creates processing problems.
Phytate/phytic acid: They bind to divalent cations such as Ca, Fe, Zn & Ma, rendering them nutritionally unavailable.
Protease inhibitors: They form complex with proteinases and rendered them inactive and thus limiting bioavailability of proteins (amino acids).
Oxalic acid: Common in sesame seeds. They bind with mineral elements in food, rendering them biologically unavailable.
Flatulence and beany flavour: Soybean, peanut meal have characteristic beany flavour which has limited the incorporation in some food system. Indigestion associated with flatus is also common in some oilseed meal.
Gossypol: This has limited the use of cottonseed.
Glucosides and glycosides: Present in a number of oil seeds .e.g. peanut, sunflower and canola.

## Slide 17
Treatment of Oilseeds to Remove Anti-nutritional Factors
Cooking- trypsin and chymotrypsin inhibitors, saponin, phytates, allergens
Fermentation- rafinnose oligosaccharides, phytates
Extraction- heamagglutinin, tannin
Filtration- phytates
Enzymatic method- rafinnose oligosaccharides

## Slide 18
Table 1: Characteristics and Uses of Vegetable Oils from Seeds and Nuts
Type of oil | Melting point | Colour | Uses
Groundnut | 26 – 32 | White/light brown | Cooking
Palm | 40 – 47 | Yellow to deep red | Cooking, soap making
Palm kernel | 20 – 28 | Yellow/white | Cooking, soap making
Coconut | 20 – 24 | White/yellow | Cooking, soap making
Cotton seed | 30 – 37 | Dark/light brown | Cooking, soap making
Sunflower | 16 – 20 | Light/yellow | Cooking, soap making
Cocoa | 45 – 50 | White, yellow | Confectionery
Soybean | 20 – 21 | Light brown | Cooking
Maize (germ) | 14 – 20 | Golden yellow | Cooking
Olive | 17 – 26 | Light brown | Cooking
Mustard | 6 – 8 | Yellow | Cooking
Sesame | 20 – 25 | Light brown | Cooking
Shea nut | Solid at rm temp/>rm temp | Yellowish-white | Medicament, cooking, traditional flavouring

## Slide 19
FIRST TEST ON OILSEEDS PROCESSING/UTILISATION
Qn. 1. Mention four oilseeds and state the uses of the vegetable oil produced from each of them. 4 marks
Qn. 2. State the importance of oilseed drying before Processing / Storage. 4 marks
Qn. 3. Enumerate by means of a flow chart only, operations involved in the extraction of crude oil from a named oilseed. 2 marks
Qn. 4. Briefly explain the importance of each step of operation involved in oil refining. 10 marks

## Slide 20
OILSEED PROTEIN
Many oil producing plants contain an appreciable level of protein (especially the defatted cake/flour after oil extraction) which has great potential for use in human diet. Soybean is known to be the best protein source among the oil producing plants.
The proteins found in seeds are classified as:
Biologically active (e.g enzymes) protein,
Structural protein or
Storage/reserved protein: These are the prominent proteins in seeds and are a major resource for the nutrition of man and livestock. Therefore, they are of utmost interest when using these protein sources for human consumption.
LECTURE 4

## Slide 21
Table 2: Some oil producing crops and their major storage proteins
Botanical Name | Common Name | Major Storage Proteins
Brassica species | Canola/Rapeseed | Cruciferin or 12S protein
Zea mays | Corn | Zein
Gossypium species | Cotton seed | 11S protein
Linum ulsitatissinum L | Flax seed | 12S protein
Cannabis sativa L | Hemp | 12S protein
Arachis hypogea L | Peanut | Arachin
Carthamus tinctorius L | Safflower | Carmin
Sesamum indicum | Sesame | α globulin
Glycine Max | Soybean | Glycinin
Helianthus annuus | Sunflower | Helianthin

## Slide 22
Production of Oilseed Protein Concentrates
Oilseed protein concentrate are prepared from defatted flakes or flour by removing the water soluble non-protein constituents (e.g oligosaccharides, part of ash). They contain not less than 70% protein on a moisture free basis.
The objective in producing PCs especially, Soy protein concentrates (SPCs) is to remove strong flavour components and the flatulence sugars (stachynose and raffinose) and to concentrate the protein and dietary fibre contents (Lucas and Riaz 1995).
Three processes may be used:
heating the white flakes resulting in denaturation of the protein and they become water insoluble before the extraction process begins. Drawback- the protein has lost most of its functional properties; this method is no longer used today;
extraction with water at isoelectric pH (4.5) where the soy protein has its lowest possible solubility characteristics which can be restored by neutralization to the neutral pH.
best tasting and most functional SPCs that have found applications in the preparation of fat emulsions;
(3) extraction with aqueous (70-90%) ethyl alcohol to remove the oligosaccharides- This process is based on the (irreversible) alcoholic denaturation of the protein.
most popular; results in the most bland tasting and nutritionally most attractive SPCs.

## Slide 23
Table 3: Composition of a typical food grade soy protein concentrate
Constituent | Composition
Protein | 70% minimum
Moisture | 8% maximum
Crude fibre | 4.5 % maximum
Ash | 7% maximum
Fat | 1% maximum
Particle size | 95% < 150 microns
Standard plate count | 15000/g maximum
Salmonella in 200 g | Negative
E. coli in g | Negative

## Slide 24
Production of Oilseed Protein Isolates: Soy Protein Isolate (SPIs)
Protein isolates are more refined than concentrates, they contain 90% or more protein. The production consists of an aqueous solubulization of protein and carbohydrates at alkaline pH and the recovery of the solubilized protein, separation and, optionally washing and neutralization before drying (Moure et al., 2006).
Three steps are involved in the process of making SPIs.
(1) the soy flakes or flour are slurried with water under alkaline conditions (pH 6.8-10 at 27-66 oC using NaOH and other food grade alkaline substances) (Lusas and Riaz, 1995; Anon, 2008b);
(2) the supernatant containing the protein and the sugars in solution is acidified with HCl or phosphoric acid (H2PO4) to pH 4.5 (minimal proteins solubility-IEP).
(3) The solubility of the precipitated protein is restored by neutralizing to alkaline pH 6.5-7.0 after re-dilution with fresh water or spray dried in its acidic form and packed in multilayer paper bags (Anon 2008b; Lusas and Riaz, 1995).

## Slide 25
Isoelectric Point- IP
The pH of a solution at which the net primary charge of a protein becomes zero. It is the pH of minimum protein solubility.
At pH > IP the surface of protein is predominantly negatively charged and therefore like charged molecules will exhibit repulsive forces.
At pH < IP the surface of the protein is predominantly positively charged and repulsion between proteins occurs.
However, at IP, the negative and positive charges cancel, repulsive electrostatic forces reduced and dispersive forces predominate. The dispersive force will cause aggregation and precipitation.

## Slide 26
Utilisation of Oilseed Protein Concentrates and Isolates in Food Industry
Protein isolates has found many applications in the food industry ranging from nutritional, sensorial, and functional purposes. Soy protein concentrates and isolates are used in products and commercially accepted than other oilseed proteins.
There uses covers the following areas:
1) Nutritional Use: demonstrated in infant formula and weaning food preparation where protein requirement are most critical (e.g for growth and other development). Soy protein contains all the essential amino acids required for human nutrition
2) Health Uses: These include lowering of plasma cholesterol and prevention of cancer, diabetes and obesity as well as protection against bowel and kidney diseases.
LECTURE 5

## Slide 27
3) Use in Bakery and confectionaries: Defatted soy flour when used at 1-3% increases absorption, improves crumb body and resiliency, enhances crust colour and improves toasting characteristics in bread and buns.
4) Use in Meat products: In food industry, soy proteins is used in comminuted meat, poultry and fish products (emulsion type sausages) to increase water and fat retention.
5) Dairy-type products: Useful ingredient in milk-like beverages and simulated dairy products
6) Miscellaneous Use: Include brew flakes (soy flakes/grits); soup, gravies and sauces, tofu, etc.
7) Functional Use: Soy protein concentrates’ water binding/absorption capacity, fat binding capacity and emulsifying properties are exploited in the production and design of convenience foods.
Utilisation of Oilseed Protein Concentrates and Isolates in Food Industry Contd.

## Slide 28
Table 4: Functional properties performed by functional proteins in food Systems
Functional property | Mode of action | Food system
Solubility | Protein solvation | Beverages
Water absorption and binding | Hydrogen bonding of water; Entrapment of water (no drip) | Meat, sausages Breads, cakes
Viscosity | Thickening; water binding | Soups, gravies
Gelation | Protein matrix formation and setting | Meats, curds, cheese
Cohesion-adhesion | Protein act as adhesive material | Meats, sausages, baked goods, pasta
Elasticity | Hydrophobic binding in gluten; Disulfide links in gels | Meats, bakery
Emulsification | Formation and stabilization of fat emulsions | Sausages, bologna, soups, cakes
Fat absorption | Binding of free fat | Meats, sausages, doughnuts
Flavor-binding | Adsorption, entrapment, release | Simulated meats, bakery etc.
Foaming | Form stable film to entrap gas | Whipped toppings, chiffon desserts, angel cakes

## Slide 29
SECOND TEST ON OILSEEDS PROCESSING/UTILISATION
Qn. 1. Mention the classes of protein found in seeds, give example where applicable. 4 marks
Qn. 2. State in tabular form, four oilseeds and the corresponding storage protein found in each. 4 marks
Qn. 3. Enumerate four functional application of protein concentrates (PCs) and isolates (PIs) in food industry. 2 marks
Qn. 4. Briefly explain the importance of isoelectric point in the production of PIs. 4 marks
Qn.5. By means of a flow diagram only, explain the production of Soy Protein Isolates (SPIs). 6 marks