## Slide 1
MODELING TOTAL DISSOLVED SOLID USING MULTIPLE LINEAR REGRESSION MODEL DEVELOPED FROM EM-34 DATA AROUND OLUSHOSUN DUMPSITE IN LAGOS, SOUTH-WEST, NIGERIA
Ameloko A. and Ayolabi E.
Department of Petroleum Engineering, Covenant University Ota, Nigeria
Department of Geosciences
University of Lagos, Lagos, Nigeria

## Slide 2: Presentation Outline
Introduction
  Background to the study
  Aim and Objectives of the study
  Literature review
Materials and method
Results and Discussion
Conclusions
References

## Slide 3: Background to the study
The management of solid waste landfills has been a major problem of our urban centers in Nigeria and other developing economies worldwide.
In these urban centres, wastes are generated daily and disposed indiscriminately in rivers and landfills without recourse to the subsurface environment, geology and their proximity to the living quarters (Ehirim et; al, 2009, Adeoti et; al, 2011).

## Slide 4
Background to the study Cont’d
Fig 1.0: Pictorial view of part the Olushosun dumpsite

## Slide 5: Aim and objectives of the study
The aim of the this research work is to assess the impact of leachates from the dumpsite on the soil and groundwater system around the study area.
The specific objectives are to:
Carry out Frequency Domain Electromagnetic [FDEM] surveys to investigate the vertical and lateral distribution of contaminants around the dumpsite.
Analyze the hydrophysical properties of water samples obtained from boreholes near the sites.
Develop predictive TDS model for the study area

## Slide 6: Literature review
Electrical and electromagnetic geophysical methods are becoming increasingly accepted tools for the initial characterization of contaminant plumes from municipal and hazardous waste landfills (Greenhouse and Harris 1983; Sweeney 1984; Greenhouse and Monier-Williams 1985 Ayolabi et.al, 2015).
Many other workers have investigated the contamination of groundwater by heavy metal around landfill site [Lee, et al., 1986, Christensen, et al., 1998, Ogundiran, and Afolabi, 2008, Ayolabi and Peters, 2004, Ayolabi and Oyelayo, 2005, Ayolabi et al., 2013, Ayolabi et.al, 2015]

## Slide 7: Materials and methods
Data Acquisition
EM data
Figure 1.2: EM-34 instrument

## Slide 8: Materials and methods cont’d
Water sample analysis
The physical properties of water tested for are their total dissolved solid (TDS), pH values, temperatures, hardness and electrical conductivity (EC).

## Slide 9: Materials and methods cont’d
Statistical analysis of data
Considering the generalised Multiple Linear Regression;
…………………. (3.0)
Where Y = Dependent variable predicted by regression model
Of the regression line

## Slide 10
Results and discussion
Figure 1.3: Satellite image of Olushosun dumpsite and surrounding areas showing water sample points and EM-34 data profiles

## Slide 11
Results and discussion Cont’d
Table 1.1: Observed mean Terrain Conductivity and TDS Parameters around the Vicinity of Olushosun Dumpsite

## Slide 12
Results and discussion Cont’d
 | Coefficients | Stand. Error | tStat | P-value | Lower 95% | Upper 95% | Lower 95% | Upper 95%
Intercept | 60.42368 | 27.2158 | 2.22016 | 0.04642 | 1.12539043 | 119.721995 | 1.1253904 | 119.721995
HD 40 | 9.579794 | 0.32902 | 29.1156 | 1.69E-12 | 8.86291053 | 10.2966793 | 8.8629105 | 10.2966793
VD 20 | 3.533745 | 0.79573 | 4.44088 | 0.00081 | 1.79999782 | 5.26749358 | 1.7999978 | 5.26754935
VD 40 | -12.7011 | 0.87967 | -14.438 | 6.008E-9 | -14.617793 | -10.784481 | -14.61779 | -10.784482
Table 1.2: Summary statistics for regression model using all data variables
………. (2)
Where;
Y = Total Dissolved Solid obtained from borehole and hand dug well water within and around the site
HD 40 =Horizontal Dipole mode data obtained at 40 m coil spacing
VD 20 =Vertical Dipole mode data obtained at 20 m coil spacing
VD 40 =Vertical Dipole mode data obtained at 40 m coil spacing

## Slide 13
linear regression equation becomes;
Results and discussion Cont’d
Table 1.3: Record of the Observed and Predicted TDS

## Slide 14
Results and discussion Cont’d
Profile locations | Coordinates | VD20(mS/m) | HD40(mS/m) | VD40(mS/m) | Observed TDS from water samples (Ayolabi et.al 2015) | Predicted TDS using proposed model
P11 | 6035120.2611N 3022131.2011E | 27.3 | 17.3 | 18 | 81 | 93.9
P1 | 6035145.0011N 3022142.3611E | 110.0 | 80.0 | 85 | 112 | 135.62
P9 | 6035140.0511N 3022138.8511E | 143.5 | 140.0 | 69 | 896 | 1037.63
P10 | 6035130.8611N 3022129.7811E | 21.3 | 22.0 | 21.5 | 81 | 73.0
Table 1.4: Observed mean Terrain Conductivity and TDS Parameters around Olushosun dumpsite obtained from Ayolabi et.al 2015
Model Validation

## Slide 15
Results and discussion Cont’d
Chart: Profile location
| P11 | P1 | P9 | P10
Observed TDS by Ayolabi et.al 2015 | 81 | 112 | 896 | 81
Predicted TDS using proposed model | 93.9 | 135.62 | 1037.63 | 73
Figure 1.4: Plot of comparism between the observed TDS by Ayolabi et.al 2015b and predicted TDS using proposed model

## Slide 16
Results and discussion Cont’d
Figure 1.5: Spatial distribution of interpolated estimated TDS around Olushosun dumpsite

## Slide 17
Results and discussion Cont’d
Figure 1.6: Spatial distribution plot of apparent soil electrical conductivity (σa − mS∕m) measured using EM34 in horizontal dipole mode: 40 m (EM34-HD 40)

## Slide 18
Results and discussion Cont’d
Figure 1.7: Spatial distribution plot of apparent soil electrical conductivity (σa − mS∕m) measured using EM34 in Vertical dipole mode: 40 m (EM34-VD 40)

## Slide 19: Conclusion
The developed TDS models can easily be deployed to determine TDS concentration in groundwater around the study areas where the terrain conductivity data is available, thus reducing the time and cost of determining and monitoring both parameters separately
The outcome of this research work will assist policy makers and environmental managers to take quality decisions required to preserve and sustain a healthy environment for mankind and the ecosystems in general, and to effectively and safely manage our natural resources

## Slide 20: References
Abu-Zeid, N., G. Bianchini, G., Santarato, and C. Vaccaro, 2004. Geochemical characterisation and geophysical mapping of landfill leachates: The Marozzo Canal case study NE Italy: Environmental Geology, 45, 439–447.
Ademola, J. A., 2008. Exposure to high background radiation level in the tin minning area of Jos Plateau, Nigeria. J. Radiol. Prot, 28: 93-99.
AGI, 2003. Earth Imager 2D Resistivity Inversion Software, version1.5.10. Advanced Geosciences, Inc. Austin, TX
Adeoti, L.., Oladele, S., Ogunlana, F. O., 2011. Geo-electrical investigation of leachate impact on groundwater: A case study of Ile-Epo Dumpsite, Lagos, Nigeria, Journal of Applied Sciences and Environmental Management, 15(2), pp 361-364.
Akinloye, M. K. and Olomo J. B., 2005. The radioactivity in some grasses in the environment of nuclear research facilities located within the OAU, Ile-Ife, Nigeria. Nig. J. Phys., 17S: 219-225.
Akoteyon I. S., Mbata U. A., Olalude G. A., 2011. Investigation of Heavy Metal Contamination in Groundwater around Land-fill Site in a Typical Sub-Urban Settlement in Alimosho, Lagos State. “J. App. Sci. in Environ. Sanitation 6(2) 155-163.
Aldecy de Almeida, S., and Shozo, S., 2008. "Evaluation on surface water quality of the influence area of the sanitary landfill." Engenharia Ambiental : Pesquisa e Tecnologia 5(2): 139-151.

## Slide 21: References
Ayolabi, E. A., 2005. Geoelectric evaluation of Olushosun landfill site, southwest Nigeria and its implications on groundwater. J Geol Soc India 66:318–322
Ayolabi, Elijah A., Ebenezer, Epelle S., Oluwatosin, Lucas B., and Adedayo Ojo, 2014a. "Geophysical and geochemical site investigation of eastern part of Lagos metropolis, southwestern Nigeria", Arabian Journal of Geosciences. DOI 10.1007/s12517-014-1688-0 8:7445–7453
Ayolabi, Elijah A., Lucas, Oluwatosin B., and Chidinma, Ifekwuna D., 2014b. "Integrated geophysical and physicochemical assessment of Olushosun sanitary landfill site, southwest Nigeria", Arabian Journal of Geosciences. DOI 10.1007/s12517-014-1486-8
Baedecker, M. J., Back, W., 1979. Hydrogeological processes and chemical reactions at a landfill: Ground Wat., 17, 429-437.
Bagchi, A., 1989. Design, construction and monitoring of sanitary landfill. John Wiley & Sons, New York.
Ball, J. M., and Stove, J. G., 2002. Pollution plume migration: Coastal Park landfill. Proc. WasteCon-2002. International water management biennial, Durban, South Africa.

## Slide 22
Thank you for listening!!!